ROVER P4 SERVICING SCHEDULES

Provisional Documents for Discussion

The following schedules have been produced by two Rover P4 owners for their own use and are published here for the guidance of other owners in preparing their own schedules. Please forward any comments and additions/amendments to webmaster@roverp4.com for update.

Whilst all owners should have to hand the servicing handbook for their car, there are two factors which have caused the derivation of these schedules.

Firstly many of our cars now cover a low annual mileage and to carry out serving on a mileage basis as originally prepared by Rover is not appropriate for example the corrosive products of combustion which collect in engine oil should not be left in place for more than one year at the most.

Secondly the cars are now over thirty five years old and items which Rover may have considered unnecessary to service for a normal lifetime now warrant extra attention if the cars are to be kept in good running order, safe and reliable.

The first schedule is a proposed minimum annual service schedule for a Rover 110 model prepared by Barry Kensett and used as the basis of the servicing workshops which he has conducted for other P4 owners. This schedule is prepared from information in all known manuals and handbooks.

The three extended servicing schedules have been compiled by Brian Griffiths from his personal experience with his Rover 95 and are recommended for use by all owners who have just purchased a Rover P4 or on an annual or mileage basis (whichever comes first) for owners requiring a more comprehensive programme.

These schedules can be used as the basis for other models by referring to the appropriate handbook and amending as necessary. The main difference between these two schedules is that one applies to an overdrive car with engine oil used in the gearbox and the other for a straight gearbox which uses gear oil.

These documents are designed to print out as six A4 sheets.

Copyright Barry Kensett & Brian Griffiths 2001

ROVER 110 ANNUAL SERVICE SCHEDULE

(Based on 3000 miles/year)

# Engine	Drain & refill sump	SAE 20W/50

Renew oil filter

Clean breather filters (2)

Check valve clearances – Inlet .006 hot, Ex .010 cold

Cooling System	Check level

Renew anti freeze (2 years)

Dynamo	Oil end bearing		SAE 20W/50

Check fan belt tension	5/16 – 7/16

Sparking Plugs	Check gap		.029 - .032

Distributor	Contact breaker		.014 - .016

Oil cam		SAE 20W/50

Lift rotor and oil		SAE 20W/50

Oil advance through base plate	SAE 20W/50

Clean and inspect cap

Fuel System	Check slow running

Check idle mixture

Top up damper		SAE 20W/50

Check fuel filter

Tuning	Check dwell angle		35 +/- 3 deg

Check timing		6 deg BTDC

Check A/R function (vacuum & centrifugal)

Check idle mixture

Check idle speed

Gearbox	Check oil level		SAE 20W/50

Change oil at 3 yrs box and o/drive	5 pints

Lubricate propshaft (2 Points)	Grease

Rear Axle	Check oil level		SAE 90

Change oil at 3 yrs		3 pints

Check U bolts

Clutch	Check free play		¾ at pedal

Steering	Check levels in steering box & relay	SAE 90

Check ball joint boots

Check swivel pins		SAE 90

Check front hubs for leakage

Brakes	Check fluid level

Check disc pads

Check rear linings and adjust

Check handbrake function & sliding in backplate

Flush fluid at 2 years

Battery	Check water level

Check terminals tightness and corrosion

Body	Lubricate hinges and locks

# Compiled Barry Kensett Revised 23 December 2001

MAJOR (24-MONTH or 12,000 mile) SERVICE

ON THE RAMP

Sump: drain renew filter and refill with low detergent 20W/50

Gearbox oil: drain and refill (90EP)

Cooling system: open heater matrix, drain, flush & refill system 50%

mixture of suitable anti-freeze and rain-water or distilled water

Wiring to horns, lights etc.: check condition and grommets etc.

Brake discs and pads: check condition

Engine and gearbox mountings: check security and condition

Steering box and relay: check oil levels (90EP)

Swivel housings: open air release plug, top up(90EP) at low pressure

Front hubs: dismantle, clean & reassemble

Suspension rubber parts: check and replace as necessary

Front spring support cups: check drainage and rustproofing

Steering ball-joints: check condition

Toe-in: check, should be 0-3mm

Hydraulic brakes: check pipes, unions and generally, change fluid;

check master cylinder and wheel cylinder seals: renew if needed

Handbrake: check adjustment, clean and grease linkages, check

warning light operation

Clutch pedal adjustment: check (19mm free movement at pedal pad)

Prop shaft sliding joint and UJs: grease and check rubber bushes to

centre bearing

Rear springs: check condition of , shackles, bushes, U-bolts,

gaiters etc.; use Coppaslip on fixing bolts and u-bolt clamps;

Rear axle differential: change oil (90EP) [3 pints] and check axle

breather operating freely

Rear brake drums: check for oil, if present, prise seal past

collar and press new one in - don’t attempt to lever out collar.

Dismantle, clean, grease & reassemble the wedge and roller system:

note that the wheel-cylinder must be able to slide up and down on

the backplate (see Workshop Manual)

Exhaust system and mountings: check throughout

Fuel tank: release drain and allow any accumulated debris to escape

Tyres: check condition and pressure: FRONT 32   REAR 28   SPARE 32

Spare wheel housing: grease hinges, oil release catch

Check for oil leaks and rectify as necessary

Sliding roof (if fitted): air-line from below to drains (4 no.)

Chassis, underside, inner wings etc.: remove wheels, clean, de-rust,

preserve, waxoyl and paint as necessary

Wheel arches, front and rear: check condition of flexible sealant

UNDER BONNET

Fan belt: check,if necessary replace or adjust tension 5/16” - 7/16”

Cooling system: check and replace any hoses if necessary - remember

the cylinder head by-pass hose (semi-hidden)

Thermostat: check, replace if necessary (alcohol/bellows type 74oC)

Radiator cap: check (pressure 4lbs / 0.3kg/cm2)

Heater hot-water valve: lubricate

Heater control cables: lubricate each end, also linkages

Brake servo: replace air filter element

Brake-fluid level warning light: check correct operation

Fuel sediment bowl: clean it and its gauze filter

Air filter: drain, clean and refill with engine oil

Dynamo end bearing: light oil SAE20

Dynamo: check  brushes and commutator segments

Crankcase breathers: clean

Tappets: check  HOT: inlet .006” (0,15mm);  exhaust .01” (0,25mm)

Ignition timing: check, should not exceed 6° BTDC

Plugs: check (NGK BR6ES) gap 0.032” (0,80mm)

Distributor: clean and oil  cam, lift rotor and oil, oil centrifugal

advance through baseplate (all SAE 20); clean and inspect cap

Distributor: check c/b points condition and gap .016” (0,40 mm)

HT and LT leads: check condition and security

Carburation: check at idle (700 rpm) CO not less than 5.3%

after 30 secs minimum at 3000 rpm   CO 2% - 3.5%

Carburettor piston damper: light oil SAE20

Throttle linkages: clean and lubricate

Check for oil leaks and rectify as necessary

Choke: check cable moves freely and warning light operates correctly

Screenwasher: purge system and re-fill, check operation and aim

Windscreen wipers and blades: check condition

Lamps: check operation of external lamps, and headlamp beam setting

INSIDE CAR

Lights & electrical items: check courtesy lights, warning lights

and dashboard-switched oil-level indicator operating correctly

Battery: check security, clean and grease terminals

Sliding roof (if fitted): check operation

IN LUGGAGE COMPARTMENT

Fuel pumps: check wiring, pipes and grommets

Check for leaks, water ingress, seal security & condition etc.

Check spare wheel access cover and release catch

Check light operates correctly

BODYWORK

Doors: airline & waxoyl to lower door hinges, check drainage holes,

check & lubricate hinges, mechanisms and check-straps;

Door-glasses: apply silicone spray (Fabsil) to draught strips

Rubber seals to all apertures: check condition and security

Sliding roof (if fitted): check lock, condition of aperture and drainage

Bonnet and boot: check & lubricate hinges and release mechanisms

Revised 12th November 2001

INTERMEDIATE (12-MONTH or 6,000 mile) SERVICE

ON THE RAMP

Sump: drain, renew filter and refill with low detergent 20W/50

Steering box and relay: check oil levels (90EP)

Wiring to horns, lights etc.: check condition and grommets etc.

Swivel housings: open air release plug, top up(90EP) at low pressure

Front hubs: dismantle, clean & reassemble

Suspension rubber parts: check and replace as necessary

Front spring support cups: check drainage and rustproofing

Steering ball-joints: check condition

Toe-in: check, should be 0-3mm

Engine and gearbox mountings: check security and condition

Hydraulic Brakes: check system generally throughout

Handbrake: check adjustment, clean and grease linkages, check

warning light operation

Clutch pedal adjustment: check (19mm free movement at pedal pad)

Sliding roof (if fitted): air-line from below to drains (4 no.)

Prop shaft sliding joint and UJs: grease

Rear axle differential: check oil (90EP] and check axle breather

Rear springs: check condition of shackles, bushes, U-bolts, gaiters

etc.; use Coppaslip on fixing bolts and u-bolt clamps

Exhaust system and mountings: check throughout

Check for oil leaks generally and rectify as necessary

Spare wheel housing: grease hinges, oil release catch

Rear brake drums: check for oil, if present, prise seal past collar and

press new one in - don’t attempt to lever out collar.  Check wedge

and roller system: note that the wheel-cylinder must be able to slide

up and down on the backplate (see Workshop Manual)

Tyres: check condition and pressure: FRONT 32   REAR 28   SPARE 32

Chassis, underside, inner wings etc.: remove wheels, clean, de-rust,

preserve, waxoyl and paint as necessary

Wheel arches, front and rear: check condition of flexible sealant

UNDER BONNET

Fan belt: check,if necessary replace or adjust tension 5/16” - 7/16”

Cooling system:  Check and replace hoses as necessary - remember

the cylinder head by-pass hose (semi-hidden)- top up with 50%

mixture of top-grade anti-freeze and rain-water or distilled water

Heater hot-water valve: lubricate

Brake servo:  check air filter element

Brake fluid: check level and operation of fluid level warning light

Crankcase breathers: clean

Air cleaner: visual check, if necessary clean and refill

Tappets: check  HOT: inlet .006” (0,15mm);  exhaust .01” (0,25mm)

Ignition: check advance, not more than 6° BTDC

Sparking Plugs: check (NGK BR6ES) gap 0.032” (0,80mm)

Distributor: check c/b points condition and gap .016” (0,40 mm)

Distributor: clean and oil cam, lift rotor and oil, oil centrifugal

advance through baseplate (all SAE 20); clean and inspect cap

HT and LT leads: check condition and security

Carburetter: check settings at idle (700 rpm) CO not less than 5.3%

after 30 secs minimum at 3000 rpm   CO 2% - 3.5%

Carburettor piston damper: light oil SAE20

Throttle linkages: clean and lubricate

Dynamo end bearing: light oil SAE20

Choke warning light: check operation

Screenwasher: purge system and re-fill, check operation and aim

Windscreen wipers and blades: check

Lamps: check all operating and headlamp beams set correctly

Check for oil leaks and rectify as necessary

INSIDE CAR

Gearbox oil: check level (90EP

Electrical items: check courtesy lights, warning lights and

dashboard-switched oil-level indicator operating correctly

Battery: check security, clean and grease terminals

Sliding roof: check operation

IN LUGGAGE COMPARTMENT

Fuel pumps: check wiring, pipes and grommets

Check for leaks, water ingress, seal security & condition etc.

Spare wheel access cover: check condition and lubricate catch

Check light operates correctly

BODYWORK

Doors: check all drainage holes running freely, clean & waxoyl lower

hinge orifices, lubricate hinges, locks, check straps etc.

Door-glasses: apply silicone spray (Fabsil) to draught strips

Rubber seals to all apertures: check condition and security

Sliding roof (if fitted): check lock, condition of aperture and drainage

Bonnet and boot: check & lubricate hinges and release mechanisms

Revised 12th November 2001

MINOR (6-MONTH or 3,000/9,000 mile) SERVICE

ON THE RAMP

Sump: drain & refill with low detergent 20W/50

Steering box and relay: check oil levels (90EP)

Swivel housings: open air release plug, top up(90EP) at low pressure

Steering ball-joints: check condition

Suspension rubber parts: check and replace as necessary

Front spring support cups: check drainage and rustproofing

Hydraulic Brakes: check system generally throughout

Handbrake: check  operation and adjustment and warning light

Prop shaft sliding joint and UJs: grease

Exhaust system: check condition and mountings

Tyres: check condition and pressure: FRONT 32   REAR 28   SPARE 32

Spare wheel housing: grease hinges, oil release catch

Check for oil leaks and rectify as necessary

Sliding roof (if fitted): air-line from below to drains (4 no.)

Wheel arches, front and rear : check condition of flexible sealant

UNDER BONNET

Fan belt: check,if necessary replace or adjust tension 5/16” - 7/16”

Cooling system: check and replace any hoses if necessary - remember

the cylinder head by-pass hose (semi-hidden) - top up with 50%

mixture of top-grade anti-freeze and rain-water or distilled water

Brake fluid: check level, and operation of fluid level warning light

Crankcase breathers: clean

Air cleaner: visual check, if necessary clean and refill

Ignition timing: check  not more than 6° BTDC

Tappets: check  HOT: inlet .006” (0,15mm);  exhaust .01” (0,25mm)

HT and LT leads: check

Sparking plugs: check (NGK BR6ES) gap 0.032” (0,80mm)

Distributor cam: clean and oil , lift rotor and oil, oil centrifugal

advance through baseplate (all SAE 20); clean and inspect cap

Distributor: check c/b points condition and gap .016” (0,40 mm)

Carburetter: check settings:  at idle (700 rpm) CO not less than 5.3%

after 30 secs minimum at 3000 rpm   CO 2% - 3.5%

Carburettor piston damper: light oil SAE20

Dynamo end bearing: light oil SAE20

Throttle linkages: clean and lubricate

Choke warning light: ensure correct operation

Screenwasher: purge system and re-fill, check operation and aim

Windscreen wipers and blades: check

Lamps: check all operating and headlamp beams set correctly

Check for oil leaks and rectify as necessary

INSIDE CAR

Gearbox oil: check level (90EP)

Electrical items: check courtesy lights, warning lights and

dashboard-switched oil-level indicator operating correctly

Battery: check security, clean and grease terminals

Sliding roof: check operation

IN LUGGAGE COMPARTMENT

Check for leaks, water ingress, seal security & condition etc.

Spare wheel access cover: check condition and lubricate catch

Check light operates correctly

BODYWORK

Doors: check all drainage holes running freely, clean & waxoyl lower

hinge orifices, lubricate hinges, locks, check straps etc.

Door-glasses: apply silicone spray (Fabsil) to draught strips

Rubber seals to all apertures: check condition and security

Sliding roof (if fitted): check lock, condition of aperture and drainage

Bonnet and boot: check & lubricate hinges and release mechanisms

Revised 12th November 2001